## Slide 1: Enabling Traditional Vision on Specialized Deep Learning Hardware
Paul Brasnett
Senior Research Manager
PowerVR Vision & AI
Notes: 1

## Slide 2: Overview
Introduction
Mapping traditional vision to deep learning primitives
Traditional vision to learning-based vision

## Slide 3: Introduction

## Slide 4: Imagination: A global technology leader
Developing innovative IP
  PowerVR GPU: leader in graphics & compute
  PowerVR Vision & AI: dedicated IP for vision & AI
  Ensigma: connectivity and broadcast communications IP
  Delivering exceptional service
  Enabling very fast time to market
  Enabling customers to leverage IP to maximise differentiation
Driving major markets
  Helping our partners to create successful solutions
  Influencing new and emerging opportunities
  Showcasing and proving our technology with real products
A technology powerhouse for multimedia and communications IP
HQ in UK
>800 people world-wide
>80% of staff are engineers
People
More than 10bn units shipped
Over 3m per day
Around 1.2bn in past year
Products

## Slide 5: Introduction
Traditional vision → deep learning
Significant investment in traditional vision
  Expect to move over to deep learning for some or all algorithms
Choices today when designing or selecting silicon
  Optimise for deep learning
  Optimise for traditional vision
  Increased cost to provide dedicated support for both
Programmable solutions available do not ‘solve’ the problem
  Still need to make a choice about priorities

## Slide 6: Embedded AI
Edge Processing on Modern System on Chip (SoC)

## Slide 7: Modern SoC
CPU
GPU
Video
Vision
Comms
ISP

## Slide 8: Traditional Vision v Deep Learning
Traditional Computer Vision
  > 30 years investment by industry
  Often good enough for specific tasks
  Proven, mature and understood
  Diverse set of primitive operations
    Lots of algorithmic secret-sauce
Deep Learning
  Huge investment over past 3-4 years
  State-of-the-art for many tasks
  New model development takes investment
  Relatively small set of basic primitives
    Although increasing

## Slide 9: Modern SoC
CPU
GPU
Video
Trad. Vision
Comms
ISP
CPU
GPU
Video
NNA
Comms
ISP
Deep Learning SoC
Traditional Computer Vision SoC

## Slide 10: Processors for Embedded Vision
DNN
Traditional Vision
Programmable
Fixed function
Maximum flexibility
Optimum performance, area and power

## Slide 11: Processors for Embedded Vision
DNN
Traditional Vision
Programmable
Fixed function
Maximum flexibility
Optimum performance, area and power
PowerVR 2NX

## Slide 12: Processors for Embedded Vision
DNN
Traditional Vision
Maximum flexibility
Optimum performance, area and power
Traditional Vision
Programmable
Fixed function

## Slide 13: PowerVR 2NX
Scalable neural network IP
  Up to 4TOp/s
Fully flexible data types support
Efficient data exchange formats for NNA to GPU/CPU
Dedicated support for all key neural network layers
Deep Learning IP

## Slide 14: PowerVR 2NX
Optimised Dataflow
Convolution
Image
Activation
Pooling
Normalization
Convolution
Image
Activation
Pooling
Normalization
PowerVR 2NX – Single Pass

## Slide 15: Deep Learning Primitives
DNN primitives
  Convolution
  Convolution transposed
  Fully Connected
  Activation
  Pooling
  Tensor Operations
  Normalisation
Expressing traditional vision using DL primitives
  Use TensorFlow, Caffe, etc.
  Run on PowerVR 2NX processor
Supported by PowerVR 2NX

## Slide 16: Support: From Frameworks to SoC
CPU
GPU
Video
NNA
Comms
ISP
PowerVR NDK
Profiler
Tuner
Adapter
Mapper

## Slide 17: Expressing traditional vision using DNN primitives

## Slide 18: Mapping Traditional Vision to DNN Primitives
Example 1: Binary Morphological Operator - Dilate
Input
Image
Structuring
Element
Output
Image

## Slide 19: Mapping Traditional Vision to DNN Primitives
Example 1: Binary Morphological Operator - Dilate
for(int i=0;i<height;i++)
for(int j=0;j<width;j++)
{
…
}
Input
Image
Structuring
Element
Output
Image

## Slide 20: Mapping Traditional Vision to DNN Primitives
Example 1: Binary Morphological Operator - Dilate
Pooling: - Max
- 3x3 window - 1x1 stride
for(int i=0;i<height;i++)
for(int j=0;j<width;j++)
{
…
}
max_pool(in,[1,3,3,1],
[1,1,1,1])
Input
Image
Structuring
Element
Output
Image

## Slide 21: Mapping Traditional Vision to DNN Primitives
Make use of convolution transpose primitives
Example 2: 2x Bilinear Up-Scaling
xn
Xn+1
Xn+2
Xn+3
f0
f1
f2
f3
ym+3
ym+2
ym+1
ym
f0
f1
f2
f3
f0
f1
f2
f3
Convolution with stride = 2

## Slide 22: Mapping Traditional Vision to DNN Primitives
Make use of convolution transpose primitives
Example 2: 2x Bilinear Up-Scaling
xn
Xn+1
Xn+2
Xn+3
f0
f1
f2
f3
ym+3
ym+2
ym+1
ym
f0
f1
f2
f3
f0
f1
f2
f3
Convolution transpose, scale factor = 2
Xn
Xn+1
f0
f1
f2
f3
ym+1
ym
f0
f1
f2
f3

## Slide 23: Mapping Traditional Vision to DNN Primitives
Example 2: 2x Bilinear Up-Scaling
Linear upscale with scaling factor = 2
Xn
Xn+1
0
0.5
1
0.5
ym+1
ym
0
0.5
1
0

## Slide 24: Mapping Traditional Vision to DNN Primitives
Example 2: 2x Bilinear Up-Scaling
2D linear upsample filter with scaling factor = 2
0.25
0.5
0.25
0.5
1
0.5
0.25
0.5
0.25
0.25
0.25
0.25
0.25
0.5
0
0.5
0
0.5
0.5
0
0
1
0
0
0
conv2d_transpose(input,[[0.25,0.5,0.25],[0.5,1.0,0.5],[0.25,0.5,0.25], [1,new_height,new_width,channels],[1,2,2,1])

## Slide 25: Mapping Traditional Vision to DNN Primitives
Example 3: Histogram
h bins
Histogram

## Slide 26: Mapping Traditional Vision to DNN Primitives
Example 3: Histogram
h bins
Histogram
1
Convolution
1
1
1
1x1x1xh filters

## Slide 27: Mapping Traditional Vision to DNN Primitives
Example 3: Histogram
h bins
Histogram
1
Convolution
1
1
1
1x1x1xh filters
Activation

## Slide 28: Mapping Traditional Vision to DNN Primitives
Example 3: Histogram
h bins
Histogram
1
Convolution
1
1
1
1x1x1xh filters
Activation
Pooling
b0
b1
b2
bh
b0
b1
b2
b3

## Slide 29: Traditional vision to learning-based vision

## Slide 30: Mapping Traditional Vision to DNN Primitives
Feature Descriptor: Brisk
BRISK sampling positions
Well-known & widely used binary image feature descriptor
Good example of traditional vision
  Hand designed, based on insights and intuition
Defined 60 samples around feature point
Set of 512 ‘short-distance’ pairs defined S
Generates a 512D patch descriptor

## Slide 31: Mapping Traditional Vision to DNN Primitives
Feature Descriptor: Brisk
Express Brisk feature pairs as (sparse) matrix
= sigmoid
Map to DNN primitives
  Fully connected (matrix-vector multiply)
  Activation

## Slide 32: Learning a Feature Descriptor: Brisk
Learning a better descriptor
Set up a trainable weight matrix
= sigmoid,
Use triplet-loss to simultaneously
  Maximise distance between different patches
  Minimise distance between same patches
Use HPatches dataset

## Slide 33: Feature Descriptor: Brisk
Result: HPatches (Easy)
Chart: Recall

## Slide 34: Example learnt ‘features’

## Slide 35: Summary

## Slide 36: Summary
Deep learning defines a set of basic primitives
  PowerVR 2NX has efficient and comprehensive support for these
Traditional computer vision can be enabled in a deep learning world by exploiting these primitives
Traditional vision algorithms can then be used as a starting point for learning
  Leverage existing investment
  Provides a path to take incremental steps into learning