## Slide 1: High-throughput object detection on Edge platforms with FPGA
Srinivasa Manohar Karlapalem
(srinivasa.m.karlapalem@intel.com)

## Slide 2: Notices and Disclaimers
Software and workloads used in performance tests may have been optimized for performance only on Intel microprocessors. Performance tests, such as SYSmark and MobileMark, are measured using specific computer systems, components, software, operations and functions. Any change to any of those factors may cause the results to vary. You should consult other information and performance tests to assist you in fully evaluating your contemplated purchases, including the performance of that product when combined with other products. For more complete information visit: http://www.intel.com/performance.
Tests document performance of components on a particular test, in specific systems. Differences in hardware, software, or configuration will affect actual performance. Consult other sources of information to evaluate performance as you consider your purchase. For more complete information about performance and benchmark results, visit www.intel.com/benchmarks.
Intel technologies’ features and benefits depend on system configuration and may require enabled hardware, software or service activation. Performance varies depending on system configuration. No computer system can be absolutely secure. Check with your system manufacturer or retailer or learn more at intel.com.
The products described may contain design defects or errors known as errata which may cause the product to deviate from published specifications. Current characterized errata are available on request.

## Slide 3: Notices and Disclaimers
FTC Optimization Notice
Optimization Notice: Intel's compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice.
Notice Revision #20110804

## Slide 4: Notices and Disclaimers
No license (express or implied, by estoppel or otherwise) to any intellectual property rights is granted by this document.
Intel disclaims all express and implied warranties, including without limitation, the implied warranties of merchantability, fitness for a particular purpose, and non-infringement, as well as any warranty arising from course of performance, course of dealing, or usage in trade.
This document contains information on products, services and/or processes in development. All information provided here is subject to change without notice. Contact your Intel representative to obtain the latest forecast, schedule, specifications and roadmaps.
The products and services described may contain defects or errors known as errata which may cause deviations from published specifications. Current characterized errata are available on request.
Copies of documents which have an order number and are referenced in this document may be obtained by calling 1-800-548-4725 or by visiting www.intel.com/design/literature.htm.
Intel, the Intel logo, Atom, Quark, Iris, Altera, Arria and Movidius are trademarks of Intel Corporation or its subsidiaries in the U.S. and/or other countries.
OpenCL and the OpenCL logo are trademarks of Apple Inc. used by permission by Khronos.
*Other names and brands may be claimed as the property of others
© 2018 Intel Corporation. All rights reserved.

## Slide 5: Outline
  Overview of Edge platforms
  Introduction to the Object-detection problem
  Edge specialized Hardware solutions: FPGA
  Solution Optimization/Tuning techniques
  Summary

## Slide 6: Overview of Edge

## Slide 7: What is ‘Edge’ platform?
“Gateway to Cloud”
  Placed on-premise and close to data source
  Data sources connect to the Cloud through them
  First receivers & analyzers of data
  Designed to endure on-field conditions while capable of complex analytics
© Intel Corporation

## Slide 8: Why do we need Edge platforms?
  Slow/Unreliable network connectivity
  Expensive cloud storage
  Expensive network connection
  Privacy/Security of customer data
© Intel Corporation

## Slide 9: Introduction to Object detection

## Slide 10: Multi-class object Detection
  Identify and locate all the objects in the picture
  Accurately locate their positon in the picture with bounding boxes
  Commonly used in Digital Surveillance, Security & Autonomous Driving applications.
  Published techniques already exist. Eg. Fast-RCNN (Girshick [2]), YOLO (Redmon, et. al. [3]), SSD (Liu et. al. [4]), etc.
Image with bounding boxes around objects
Source: Liu et. al. [4]

## Slide 11: Constraints
  Close to real time performance requirements
  Low power consumption
  Variable input image formats & resolutions
  Easily adaptable to arbitrary number of classes
  Deployable on low-memory platforms
  Maintain ‘reasonable’ accuracy
Performance
Power
Accuracy
Size

## Slide 12: Specialized hardware for the Edge

## Slide 13: Hardware choices
General Purpose
Easily programmable
Massively parallel
High throughput
High thoughput
Low power
Ultra low power
Low price
© Intel Corporation

## Slide 14: The FPGA technology
  Field Programmable Gate Array
  Comprised of digital logic elements
  can be (re)programmed ‘on the field’
Figure: Sketch of FPGA architecture
Source: Bai, Yu et. Al. [1]

## Slide 15: FPGA benefits
Source: https://www.altera.com/solutions/technology/artificial-intelligence/overview.html

## Slide 16: Intel®Arria™ 10: An OpenCL* compatible FPGA
© Intel Corporation
* OpenCL and the OpenCL logo are trademarks of Apple Inc. used by permission by Khronos.

## Slide 17: Optimization and tuning techniques

## Slide 18: Optimized FPGA logic
  Deep Learning Accelerator[5] used on Intel® Arria™ 10 FPGA.
  Optimized design greatly reduces memory transfers
  Efficiently use limited on-chip caches
  Processing Elements (PE) designed to operate on vector chunks of feature map data
DLA Stream Buffer architecture,
Aydonat et. al. [5]

## Slide 19: Use faster layers for classifier and detector
  Use SSD topology.
  Replace VGG16 [6] with the faster Squeezenet [7] as the backend classfier.
  Replace convolution layers in SSD[4] with 7 Fire layers similar to ones in Squeezenet[7].
  Overall size reduction from ~103 MB to ~25MB

## Slide 20: Reduced Input image resolution
Change input data resolution from 300x300x3 to 224x224x3
  Limit accuracy loss by connecting passing on earlier feature maps to Detection layers
  Achieved using ResNet [8] -like to bypass some intermediary layers
  Allows earlier feature maps to be concatenated to later ones
  Fairly retains accuracy in some cases without performance hit.
  Addresses vanishing gradient issues occurring from extra Fire layers in detector.

## Slide 21: ‘Fit’ Feature maps into Stream buffer
  Some intermediary feature maps too large to fit into the Stream buffer
  Cause data transfers to external memory and degrade performance
  ‘Trimming’ feature maps accordingly:
    Larger convolution filter with larger strides
    Fewer but larger convolution filters
  Size reduction with minimal accuracy loss achieved in some cases, though heavily case dependent
  Seen to also affect training time

## Slide 22: Augment with an efficient media pipeline
  Edge inference often relies on data captured and pre-processed in real-time
  ‘Pipelining’ data processing stages with inference alleviates inference performance restrictions to accommodate better accuracy
  Hardware accelerated media processing is particularly beneficial
  Solutions like Intel® Media SDK provide hardware accelerated media processing implementations.

## Slide 23: Summary

## Slide 24: Key takeaways
  Intelligent Edge analytics vital to increasingly smart, connected world.
  The versatility of FPGAs make them excellent Edge platform components.
  Edge needs software and topology optimizations custom tailored for specialized HW.
  Intel is committed to provide a streamlined experience for Edge developers to develop and deploy efficient Edge solutions.

## Slide 25: Links
  Intel® Arria™ 10 FPGA: www.altera.com
  Intel® FPGA software: https://www.altera.com/solutions/technology/artificial-intelligence/software.html
  Intel® Media SDK: https://software.intel.com/media-sdk
  Intel® open-sourced topologies: https://github.com/intel/Edge-optimized-models
  More details at Intel® AI: https://ai.intel.com
    Lookout for Intel® AI DevCon 2018

## Slide 26: Citations & References
  Bai, Yu & Alawad, Mohammed & F. DeMara, Ronald & Lin, Mingjie. (2015). Optimally Fortifying Logic Reliability through Criticality Ranking. Electronics. 4. 150-172. 10.3390/electronics4010150.
  Girshick, Ross. Fast-RCNN. arXiv:1504.08083 [cs.CV]
  Redmon, Joseph & Divvala, Santosh & Girshick, Ross & Farhadi, Ali. You Only Look Once: Unified, Real-Tiem Object Detection. arXiv:1506.02640 [cs.CV]
  Liu et. al. SSD: Single Shot MultiBox Detector. arXiv:1512.02325 [cs.CV]
  Aydonat et. al. An OpenCL(TM) Deep Learning Accelerator on Arria 10. arXiv:1701.03534 [cs.DC]
  Simonyan et. al. Very Deep Convolutional Networks for Large-Scale Image Recognition. arXiv:1409.1556 [cs.CV]
  Iandola et. al. SqueezeNet: AlexNet-level accuracy with 50x fewer parameters and <0.5MB model size. arXiv:1602.07360 [cs.CV]
  He et. al. Deep Residual Learning for Image Recognition. arXiv:1512.03385 [cs.CV]

## Slide 27: Questions?

## Slide 28: Contact Srinivasa Manohar Karlapalem srinivasa.m.karlapalem@intel.com

## Slide 30
Don’t forget to share your opinions!
We value your opinions. You’re feedback about this session is very important.
Scan the QR code from your mobile device to answer a 5-question survey and be entered into a drawing for a chance to win a $100 American Express Gift Card.
Winners will be notified via email on May 15, 2018. Your response will be anonymous and used in summary form only. Information collected will not be used for promotional or sales purposes.
Privacy policy: http://www.exhibitsurveys.com/privacy
Survey is conducted by Exhibit Surveys, Inc. and is not affiliated with the 2018 Artificial Intelligence Conference or O’Reilly Media, Inc.
SAMPLE
Notes: Speakers please announce: “Just a reminder before you leave: Please complete the short online survey about this session. Your opinions are important to us at Intel AI, and you’ll have a chance to win a $100 AMEX gift card.”